## Slide 2
Modelling synchrotron radiation beamlines with
OASYS
Transport of coherence in a Beamline
Manuel Sanchez del Rio
srio@esrf.fr
Advanced Analysis & Precision Unit, MEG/ISDD, ESRF
March 21st 2025
WOFRY

## Slide 3: Transport of coherence in a Beamline
Outline:
Introduction coherence in X-ray beams
Simple cases of diffraction by slits
Partial coherence concepts
  Coherence Fraction
  Coherent Mode Decomposition
  Example
WOFRY

## Slide 4: Coherence – Basic concepts
Coherence: is the ability of a beam to be diffracted by objects (e.g. slits) producing a “diffraction pattern”
Diffraction pattern results from the interference of propagated electric fields
1 m
15 m
Ray tracing
MODEL 1

## Slide 5: Coherence – Longitudinal and transversal
Longitudinal or Temporal Coherence: depends on the monochromaticity of the source (describes the correlation or predictable relationship between waves observed at different moments in time)
Transversal Coherence: Depends on the source geometry (correlation between waves at different points in space)
We need at least TWO waves for defining coherence parameters

## Slide 6: Diffraction by slits (fully coherence)
Aperture=0.4 mm, E=17225 eV, D=5cm
F=D
F=D/2
F=D/2
Converging spherical +
Propagation (D)
Plane + Lens (F=D)+ Propagation (D)
Spherical divergent+ Lens (F=D/2)+ Propagation (D)
Gaussian+ Propagation(D)+ Lens (F=D/2)+ Propagation (D)
MODEL 2.1
MODEL 2.2
MODEL 2.3
MODEL 2.4

## Slide 7: Coherent Fraction (partial coherence)
CF: Ratio of the good photons (coherent) over the total amount of photons
CF=1 for a coherent source and 0 for an incoherent one
Beams are treated with:
  “wave optics” if they are coherent
  “ray tracing” if they are incoherent
  “coherent mode decomposition”1 if they are partially coherent
The CF can be calculated:
  From the ratio of the phase space: “coherent source” / “actual source”
  Occupation of the first coherent mode
Consequences:
  Storage ring with zero emittance has CF=1 (Diffraction Limited Storage Ring)
  Small emittance implies better coherence
  CF decreases when photon energy increases
It was CF~10-3, 10-4 for ESRF1 and CF~10-2 FOR EBS

## Slide 8: Example: U17 @ 15 keV
CFv=0.97
CFv=0.54
CFh=0.53
CFh=0.07
Horizontal
Vertical
50x50 mm2
Modes Cumulated occupation
Modes Cumulated occupation
CF= CFh x CFv:
Source: 0.038
Image: 0.51
MODEL 3

## Slide 9: Example: U17 @ 15 keV Coherence gain by closing slit

## Slide 10
CFh=0.53
Additional slides

## Slide 11: Coherent radiation produces interference patterns
INTERFERENCE DIFFRACTION

## Slide 12: Coherence – Longitudinal and transversal
Starting with TWO well defined (thus coherent) waves with THE SAME intensity:
LONGITUDINAL (TEMPORAL) COHERENCE LENGTH LL
Distance over which two waves from the same source point with slightly different wavelengths will completely dephase.
TRANSVERSE COHERENCE LENGTH LT
The lateral distance along a wavefront over which there is a complete dephasing between two waves of the same wavelength, which originate from two separate points in space
COHERENT LENGTHS - TWO WAVES http://www.csrri.iit.edu/~segre/phys570/10F/lecture_04.pdf

## Slide 13: LONGITUDINAL COHERENCE for a typical synchrotron
the synchrotron beam is not formed by two single monochromatic plane waves
But we give some approximated values…
Imagine that a typical monochromator:
  Produces a typical of ∆λ/λ = 10−4 (Si 111) peak distribution (Gaussian)
  For main wavelength of λ = 1Å we select two lines thus separated its width ∆λ = 10−4 Å
  The wavefronts of these two monochromatic waves are plane and identical
STATIONARY: This correlation time is much smaller than “bunch time” ~ 15 10-3 / c ~10-12 s~ ps

## Slide 14: LONGITUDINAL COHERENCE for a typical synchrotron
An experiment takes place typically at R = 30 m from the source
For the transversal coherence length we need some “source size”. We suppose two point sources separated by D=FWHM and R>>D in such a way that wavefronts from these two points are plane waves
LT =l R / (2D)
 | sigma um | FWHM um | LT um
V Hbeta | 3.5 | 8.2 | 182.4
V Lbeta | 3.5 | 8.2 | 182.4
V EBS | 3.4 | 8.0 | 187.7
H Hbeta | 388 | 911.8 | 1.6
H Lbeta | 37 | 87.0 | 17.3
H EBS | 27 | 63.5 | 23.6
1 mm
Hb
Lb
EBS

## Slide 15: FRESNEL DIFFRACTION
Numeric calculation: convolution with a Gaussian kernel
CONVOLUTION